## Slide 1: Level 1 SIT & SHAKE
Level 2
STRETCH & POINT
Level 3
STAND
Level 4
MARCH&WALK
BMAT Level
If patient does NOT PASS Sit & Shake Assessment, consider the following equipment:
- Ceiling or portable lift
- Comfort Glide or PATRAN sheet
SPH Equipment
If patient does NOT PASS Stretch & Point Assessment: they are considered a Level 1.
If the patient PASSES, consider the following equipment:
- Ceiling or portable lift
- Comfort Glide or PATRAN sheet
- Mechanical Sit- Stand
If patient does NOT PASS Stand Assessment, they are considered a level 2.
If the patient PASSES consider the following equipment:
- Gait Belt
- Manual Stand-aid
If patient does NOT PASS March & Walk Assessment, they are considered a Level 3.
If the patient PASSES the March & Walk Assessment, they are considered a Level 4.
Dependent/Bedfast: on bedrest, unable to assist, weakness throughout all extremities, unable to sit up.
Minimum Assist: passed level 2 assessment, able to bear weight, needs standby to minimal assistance.
* If patient uses an assistive device at baseline, Level 3 is the highest level they can be.
Moderately Dependent/Chairfast: passed level 1 assessment, can come to a seated position but cannot stand or transfer, able to bend/flex at ankle and point toes.
* May be performed with only one leg
Independent: passed level 3 assessment, able to ambulate and transfer independently without assistive devices and no physiological concerns for falling.
Patient’s Abilities
When in doubt, err on the side of caution – always default to the safest BMAT level and lifting/transfer method.
Assessment of:
Cognition
Trunk Strength
Seated Balance
Assessment of:
Lower extremity strength
Stability
Assessment of:
Lower extremity strength when standing
Assessment of:
Standing balance
Gait
Why?
Determine patient’s baseline prior to admission: Is assistive equipment needed?

## Slide 2: Level 1 SIT & SHAKE
Level 2
STRETCH & POINT
Level 3
STAND
Level 4
MARCH&WALK
BMAT Level
If patient does NOT PASS Sit & Shake Assessment, consider the following equipment:
- Ceiling or portable lift
- Comfort Glide or PATRAN sheet
SPH Equipment
If the patient PASSES, consider the following equipment:
- Ceiling or portable lift
- Comfort Glide or PATRAN sheet
- Mechanical Sit- Stand
If the patient PASSES consider the following equipment:
- Gait Belt
- Manual Stand-aid
- Walker
If the patient PASSES the March & Walk Assessment, they are considered a Level 4.
Dependent/Bedfast: on bedrest, unable to assist, weakness throughout all extremities, unable to sit up.
Minimum Assist: passed level 2 assessment, able to bear weight, needs standby to minimal assistance.
* If patient uses an assistive device at baseline, Level 3 is the highest level they can be.
Moderately Dependent/Chairfast: passed level 1 assessment, can come to a seated position but cannot stand or transfer, able to bend/flex at ankle and point toes.
* May be performed with only one leg
Independent: passed level 3 assessment, able to ambulate and transfer independently without assistive devices and no physiological concerns for falling.
Patient’s Abilities
When in doubt, err on the side of caution – always default to the safest BMAT level and lifting/transfer method.
Determine patient’s baseline prior to admission: Is assistive equipment needed?
Mobility
-Hoyer lift to chair
-Lateral transfer to chair
-BED ROM with caregiver
-Hoyer lift to chair
-Lateral transfer to chair
-BED ROM with caregiver
-Sitting EOB with support/supervision
-Standing/transfer with mechanical sit- stand (must be performed with PT first)
-Stand with stand aide and transfer to chair
-Stand/transfer/walk with walker distance as able
-Stand/walk with gait belt distance as able
This patient is independent without a device. Be sure to encourage mobility 3x/day and document mobility when it is observed.